## Slide 1: SoC Verification and Automation at Arm Ltd.
Final Internship Presentation
Reyansh Gahlot | 102206005
B.E. Electronics &amp; Communication Engineering
Thapar Institute of Engineering &amp; Technology, Patiala
January 2026 – June 2026

## Slide 2: Agenda
Organisation & Team Overview
Project 1: Status Register Checker
Project 2: Compile Warning Resolution
Project 3: CMN Clock Controller Integration
Project 4: AI Agent for HW Code Generation
Results & Impact
SDG Alignment
Conclusion & Future Scope

## Slide 3: Organisation Overview
Arm Ltd. – World's leading semiconductor IP company
Bangalore Design Centre – CPU Verification Group
Interconnect Team – CMN (Coherent Mesh Network) verification
~50 engineers across verification, design, architecture
Methodology: UVM 1.2 + SystemVerilog + Constrained Random
Tools: Synopsys VCS, Verdi, VC Formal

## Slide 4: Coherent Mesh Network (CMN)
Arm's scalable interconnect IP for multi-core SoCs
2D mesh topology: Cross-Points (XP) + Functional Nodes
Protocols: CHI (coherent), AXI4 (high-BW), APB (peripheral)
Node types: RN-F (CPU), HN-F (Home), SN-F (Memory), RN-I (I/O)
Features: System Level Cache, Snoop Filter, QoS, Power Mgmt
Verification challenge: Combinatorial routing paths + coherency

## Slide 5: Project 1: Status Register Checker
Problem: Manual register verification – incomplete, unscalable
Solution: Automated UVM checker with Python log parser
Architecture: Log Parser → sim_opts → UVM Scoreboard → Pass/Fail
Key Innovation: Timestamp-keyed comparison (not FIFO)
Integration: UVM factory override – zero existing code changes
Result: Found pre-existing bug undetected across multiple tape-outs

## Slide 6: Status Register Checker – Technical Details
Python Parser: Streams multi-GB logs, compiled regex, O(1) lookup
Throughput: ~500 MB/s (10 GB file in ~20 seconds)
UVM Scoreboard: Associative array indexed by simulation time
Timestamp sync: Calibration write + offset computation + tolerance
Bug found: TRACE_ACTIVE bit not deasserting on buffer-full
50,000+ automated checks per regression, zero false positives

## Slide 7: Project 2: Compile Warning Resolution
Goal: Zero-warning compilation across all 8 build configurations
Scope: 153 warnings across 47 files
Categories: Unused vars (42), Type conv (35), Deprecated (28), Uninitialised (23), Port width (16), Unreachable (9)
Methodology: 6-step process (Categorise → RCA → Fix → Test → Regress → Review)
Lesson: Port-width fix caused regression – always check ALL configs
Outcome: Zero warnings, CI policy adopted to block new warnings

## Slide 8: Project 3: CMN Clock Controller Integration
Goal: Verify clock controller for dynamic power management
5 clock domains: mesh, device, SLC, debug, always-on
6-state FSM: RUNNING → GATE_REQ → GATED → WAKE_REQ → RESTORING → RUNNING
14 CDC crossings verified (structural + functional + formal)
Q-Channel protocol interface to system PMU
Constraints: Wake-up ≤32 cycles, quiescence timeout 1000 cycles

## Slide 9: Clock Controller – Bug Discoveries
Bug 1: Missing 2-FF synchroniser on CDC-12 path
  • clk_debug → clk_mesh status signal had no sync stage
  • Found by structural CDC analysis (VC Formal)
  • Confirmed via metastability injection simulation
Bug 2: Incorrect snoop priority in FSM
  • Snoop during GATE_REQUEST → FSM aborts correctly
  • But QACCEPTn not deasserted → PMU state corruption
  • Could cause permanent clock-on (power waste)
Both Severity 2 – would affect silicon in power scenarios

## Slide 10: Project 4: AI Agent for HW Code Generation
Problem: New RTL → 2-3 days manual programming code writing
Solution: 4-stage AI pipeline (automated, validated)
Stage 1: RTL Parsing (extract register map from SystemVerilog)
Stage 2: Context Retrieval (RAG from spec database)
Stage 3: LLM Code Generation (structured prompts)
Stage 4: Validation (cross-check addresses against RTL)
Integrated into CI/CD – triggers on RTL commit

## Slide 11: AI Agent – Results
Time per IP block: 2-3 days → < 1 hour (40x faster)
Register address errors: 2-5 per block → 0 (100% elimination)
Code coverage: 85-90% → 99% (+10-14%)
Review iterations: 3-4 rounds → 1-2 rounds (60% reduction)
Deployed on 3 IP blocks: 4,200 lines generated, 0 address errors
Key: Ground-truth validation prevents hallucination
Human-in-the-loop: PR for engineer review, not auto-commit

## Slide 12: Summary of Results
Project 1: 50K+ automated checks/regression, 1 pre-existing bug found
Project 2: 153 warnings → 0, zero-warning CI policy adopted
Project 3: 14 CDC paths verified, 2 RTL bugs found (Sev 2)
Project 4: 40x time reduction, 0 address errors
Total bugs found: 3 (all Severity 2 – would affect silicon)
Estimated cost avoidance: $3-10 million (re-spin prevention)
Engineer hours saved: ~200/year via AI agent

## Slide 13: Impact Analysis – UN SDGs
SDG 9: Industry, Innovation & Infrastructure
  • Verified silicon powers global digital infrastructure
  • AI agent fosters innovation in semiconductor workflows
  • Reliable processors for healthcare, finance, transport
SDG 12: Responsible Consumption & Production
  • 3 bugs caught pre-silicon → avoids wasteful re-spins
  • Clock gating → 15-30% dynamic power reduction
  • Extends device battery life → reduces e-waste
  • Bug at simulation: $1 | at fabrication: $1M | deployed: $1B

## Slide 14: Challenges & Learnings
Technical: 800-page CHI spec, timestamp sync iterations, CDC formal tools
Process: 500K+ line codebase, regression incident on 'trivial' fix
Professional: Agile workflow, code review discipline, multi-stakeholder
Key Learnings:
  Automated infrastructure provides lasting value (amortised ROI)
  Always validate across ALL configurations
  AI + validation = trust (ground-truth prevents hallucination)
  Minimal change principle prevents collateral damage

## Slide 15: Future Scope
Status Checker: Extend to performance counters, formal reg verification
Clock Controller: DVFS interactions, ML-based CDC scenario generation
AI Agent: Generate testbench code (not just programming sequences)
  • Multi-agent architecture for specialised generation tasks
  • Feedback loop: simulation results → improve generation
Broader: AI-assisted verification paradigm shift
  • Boundary between human judgement and automation continues to shift
  • Applicable across semiconductor industry

## Slide 16: Thank You
Reyansh Gahlot | 102206005
Faculty Mentor: Dr. Amit Mishra (TIET, Patiala)
Industry Mentor: Vinod Ramanujam (Arm Ltd., Bangalore)
Questions?